## Slide 1
PMFS: source localization by map comparison
b
Online candidate-source predictions
Local wind + floor plan
GMRF wind estimate
2D filament model
s
Stochastic transport
Predicted hit maps
s₁
s₂
fˢᵢ = p(Hᵢ | S = s)
Coarse-to-fine source refinement
c
Confidence-weighted map comparison
Measured
Predicted
Same cells, different sources
Compare each cell
1 − αᵢ |fᶻᵢ − fˢᵢ|
Multiply & normalize
Source probability
p(S | H)
d
Next sampling location
Plume variation
Source weights
Low confidence
ψᵢ = (1 − αᵢ) Varₚ(fˢᵢ)
Initial exploration
a
Measured environment
Gas readings
Hit / miss
Robot positions
Gas-hit probability
fᶻᵢ = p(Hᵢ | Z)
Sampling confidence αᵢ
Move, sample gas and wind, update maps
Schematic maps · Original PMFS, IEEE T-RO 2024
Obstacle
Sample
Notes: Original PMFS principle. Reference: Ojeda, Monroy and Gonzalez-Jimenez, Robotic Gas Source Localization with Probabilistic Mapping and Online Dispersion Simulation, IEEE Transactions on Robotics (2024), https://arxiv.org/html/2304.08879v3. The diagram summarizes Sections III–V, equations 7–12. Colored grids and traces are schematic, not measurements or experimental results. The source probability is normalized over candidate source cells; a gas-hit probability is a different quantity. Original planning uses confidence-modulated, source-weighted prediction variance, after an initial exploration phase. Current upstream code also contains later mutual-information changes; these are not depicted. This diagram does not claim guaranteed source identifiability. All shapes are native PPT objects, no generated or downloaded pictorial images are included.